| Parameter | Standard Observed |
| --- | --- |
| Mechanical Shock | MIL-STD-202 Method 213, Condition C |
| Vibration | MIL-STD-202 Method 201, 204, and 214 |
| Solderability | IPC/EIA-STD-002A |

Precision Devices INC. – 8840N. Greenview Drive, Middleton WI 53562, Tel- 1-800-274-XTAL, Fax- 1-608-831-3343,

www.pdixtal.com  Outside US Phone- 608-381-4445, E-mail- sales@pdixtal.com

PD (HK) Ltd. – Tel- (852)-2367-3626, Fax- (852)-2646-3122, E-mail- sales@pdixtal.com.hk

PD (UK) Ltd. – Tel- +44 (0)1223 834444, Fax- +44(0)1223 834589, E-mail- sales@pdixtal.co.uk

# Text boxes

TEMPERATURE COMPENSATED CRYSTAL OSCILLATOR (TCXO)

### TC23-3

The TC23-3 series provides a range of high frequency, temperature compensated crystal oscillators, packaged in a robust, high reliability enclosure. The outputs are matched directly into 50and the series provides first class performance and accuracy with the option of voltage control or mechanical adjustment.

## ADVANTAGES

Through Hole

50( Termination

Hermetic Package

400MHz Operating Frequency

## APPLICATIONS

Telecommunications

Base Stations

Test Systems

Instrumentation

| PARAMETER | MINIMUM | MAXIMUM | UNITS |
| --- | --- | --- | --- |
| NOMINAL FREQUENCY (Fo) | 20 | 400 | MHz |
| CALIBRATION TOLERANCE | -1.0 | +1.0 | ppm |
| FREQUENCY STABILITY Over Temperature Range (See Note 2) Ageing (per year at +25C) Over Supply Voltage Variation (Vcc = +5.0V ±5.0%) | -1.0 -1.0 -0.3 | +1.0 +1.0 +0.3 | ppm |
| OPERATING TEMPERATURE RANGE (See Note 2) | 0 | +50 | C |
| STORAGE TEMPERATURE RANGE | -40 | +85 | C |
| SUPPLY VOLTAGE (Vcc) (See Note 2) | +2.85 | +3.15 | V |
| SUPPLY CURRENT (Dependant upon nominal frequency) | 10 | 30 | mA |
| OUTPUT WAVEFORM A.C. COUPLED SINEWAVE Amplitude Harmonic Distortion Sub-harmonic Distortion Spurious | 0 | +5 -15 -30 -65 | dBm dBc dBc dBc |
| FREQUENCY ADJUSTMENT (Internal trimmer) (Order Code TC23-5T) | (2.0 |  | ppm |
| VOLTAGE CONTROL +2.5V ±2.0V (Order Code TC23-5V) | ±5 |  | ppm |

ELECTRICAL PERFORMANCE  (Ta=25°c, RL = 50 and Vcc = +5.0V)

NOTES   1) To order, state part number, options and nominal frequency e.g. TC23-3T 100.000MHz

2) Other temperature ranges, stabilities and supply voltages are readily available upon request.

3) Other specifications available upon request.